## Slide 1: CT EEB x1931-7 HDD/CDD Update Study Saroj Karki, ERS December 16th, 2020

## Slide 2: Agenda
Study Background
Detailed Tasks
Study Objectives
2
Schedule and Budget

## Slide 3: Study Background
HDD – Heating Degree Days
CDD – Cooling Degree Days
NOAA – National Oceanic and Atmospheric Administration
TRM – Technical Reference Manual
TMY – Typical Meteorological Year
Coastal/inland differentiation for HDD/CDD
  R91 study recommendation
  Our analysis of TMY data shows that inland HDDs are 12% greater than coastal; inland CDDs are 9% greater than coastal
    Estimate that approximately 20% of residential program participation is classified as coastal
  Other TRMs offer varying DD values by geography: NY, Mid-Atlantic TRMs
  Secondary observation: Current PSD values consider NOAA weather, 1979-2008. Other jurisdictions are updating typical weather to reflect recent climate changes.
  Measures in the PSD that use HDD/CDD values:
    Heat pump (to calculate equivalent full load hours)
    Package terminal heat pump (to calculate equivalent full load hours)
    Insulate attic openings
    Wall insulation
    Ceiling insulation
    Floor insulation

## Slide 4: Study Objectives
The objectives of this study are to:
Develop utility-specific HDD and CDD values based on the most recent climate data and recent program participation records.
  Note: we will give special consideration in the calculation of HDDs to the UI gas entities that are not coastal.
Alternative 1: Develop a single statewide set of weighted HDD and CDD values.
Alternative 2: Develop separate HDD and CDD values for inland and coastal regions.

## Slide 5: Detailed Tasks
Task 1: Weather Data Collection and Revision of HDD and CDD values
  Gather 2005-present weather data for NOAA’s 10 weather stations in CT.
  Gather recent participation data for weatherization measures offered under HES and HES-IE
  programs – Leverage existing data from x1939 data request.
  Allocate measure participation counts to each of the 10 weather stations by proximity.
  By weighting the weather data by count by station for each utilities, develop utility-specific HDD and CDD values.
    Develop alternative sets of HDD/CDD values: a single statewide set and separate inland and coastal values.
Task 2: Final Report and Presentation
  Deliver utility-specific HDD/CDD values
    Alternative 1: Develop a single statewide set of weighted values.
    Alternative 2: Develop separate inland and coastal values.
  Develop a draft and final memo report summarizing study results and updated values.
  Present study results and recommendations via a teleconference.

## Slide 6: Study Objectives and Outcomes
Objective | Method | Outcomes
Develop utility-specific HDD and CDD values. | Gather historical hourly climate data (2005-present) for NOAA’s ten weather stations across Connecticut. For each program administrator (Eversource and UI), allocate participation counts of applicable measures to each of the 10 weather stations by proximity. By weighting the CT weather data by count by station, calculate statewide HDD and CDD values for Eversource and UI. | A set of revised HDD and CDD values for Eversource A set of revised HDD and CDD values for UI
Alternative 1: Develop a single statewide set of HDD and CDD values. | By weighting the CT weather data by count by station, calculate statewide inland and coastal HDD and CDD values. | Separate HDD and CDD values for inland and coastal regions.
Alternative 2: Develop HDD and CDD values for inland coastal regions. | By weighting the CT weather data by count by station, calculate a single set of statewide weighted HDD and CDD values. | A single statewide set of HDD and CDD values.
Note: The HDD and CDD values developed under this study will be calculated assuming a residential balance temperature of 65 °F. The values will not be applicable to commercial buildings that may warrant a different balance temperature.

## Slide 7: Schedule and budget
December 2020: Study kickoff
January 2021: Literature review
February 2021 – March 2021: Research synthesis
April 2021: Final report and presentation
Reports finalized for June PSD update
Estimated Budget – $9.9k

## Slide 8: Thank You
8

## Slide 9
Saroj Karki, Project Engineer II
skarki@ers-inc.com
978-521-6233
ERS is an energy and engineering consulting firm providing services in energy efficiency customer engagement, implementation, evaluation, both pre- and post-installation M&V, custom feasibility studies, and distributed and renewable generation assessment.